## Slide 1
RIVERSIDE NEIGHBORHOOD
Drainage IMPROVEMENTS
Public Meeting #1
April 15th, 2026

## Slide 2: Introductions
In partnership with:
Scott Turner, PE, FAICP
Sarah Frisbee, EIT
Sage Hardesty
Funding provided by:
Housing Choice Grant
Community Development Block Grant
Notes: Erik

## Slide 3: Agenda
Project Summary & Background
  Existing Conditions Analysis
  Proposed Flood Mitigation
  Future Climate Considerations
  Next Steps

## Slide 4
What We Did:
Developed an existing conditions stormwater model to understand the extent and impacts of current stormwater flooding within the Riverside Neighborhood.
Developed a proposed drainage improvement plan to expand stormwater infrastructure and reduce flood risk created by rainfall in flood-prone areas.
Simulated the proposed plan to evaluate the plan’s performance vs existing conditions.
What We’re Doing:
Gathering stakeholder feedback and evaluating next steps.
Project summary & BACKGROUND

## Slide 5
PROJECT AREA
N
TOTAL PROJECT AREA
22 acres
LIMITED DRAINAGE SYSTEM
11 Manholes
41 Catch basins
11 Outfalls
~4200 Linear Feet of Conduit
Existing Streets less than 1% slope

## Slide 6
The Riverside Neighborhood has a history of flooding during significant inland and coastal storm events.
Flooding Facts:
“The number of flood events has tripled from the late 1990’s to the mid 2010’s”
“Boston has seen ~5.4 inches of sea level rise since 1995.”
*Data sourced from Building Adaptive Capacity in Revere,
Woods Hole Group
Project background – Flooding History
Mills Ave – December 2022
The Riverside Neighborhood…
Is a low-lying, flat residential coastal area
Is affected by high tides and storm surge events
Is vulnerable to future impacts of sea level rise
Has a limited and undersized drainage systems

## Slide 7
Coastal flooding, where wind, tides, waves, and storm surge lead to flooding of low-lying coastal areas.
Type of Flooding
The Riverside Neighborhood is vulnerable to two types of flooding:
Stormwater flooding, where rainfall overwhelms the capacity of the stormwater system causing it to overflow onto the road.

## Slide 8
Flood recurrence interval
Recurrence Interval: The average number of years, over the long term, between subsequent events
25-year storm occurs on average once every 25 years.
% Annual Chance: the probability of a particular flood event happening in any given year
% Annual Chance = 100/recurrence interval
25-year storm: 100/25 = 4% Annual Chance
% Annual Chance is just a probability! It is possible for a given flood to occur twice in one year, in back-to-back years, or not at all for a period of years.
25 Year Flood: You have a jar with 100 marbles – 75 clear and 25 red. There is a 1 in 25 (or 4% chance) of you reaching into your jar and pulling out the red marble.

## Slide 9
Existing Conditions PCSWMM Model
Developed stormwater model.
Delineated watersheds (in orange) contributing runoff to Riverside stormwater infrastructure system.
Produced results for 1-year, 2-year, and 10-year storm events.
Validated results based on prior observed conditions.

## Slide 10
Existing conditions 1-yr storm
During the 1-YR event, the model reveals minor flooding on Mills Ave., Gilbert Ave., River Ave. and Thayer Ave.

## Slide 11
Existing conditions 2-yr storm
During the 2-YR event, the model reveals additional flooding on Mills Ave., Gilbert Ave., River Ave., and Thayer Ave.

## Slide 12
Existing conditions 10-yr storm
During the 10-YR event, the model reveals worsening conditions in all previous flooded areas.
Flood conditions expand to Beckert, Lawson, and Franklin Avenues.

## Slide 13
Some roadways within Riverside neighborhood do not have catch basins to capture runoff or relieve flood condition.
The existing stormwater system is undersized and surcharges during frequently occurring, small intensity rainfall events (1- & 2-year events).
As precipitation events increase (10-year) the stormwater system becomes further limited and flood conditions expand to other affected roadways.
Rainfall intensity and sea levels are predicted to increase under a changing climate, resulting in worsening existing conditions.
Current climate Existing Conditions results summary

## Slide 14
Several iterations or drainage improvements were analyzed, and the following improvements were selected:
Expand Drainage System Coverage to all roadways
Increase Pipe Sizes along Mills Avenue
Increase pipe sizes throughout the project area
Install Two New Large Outfalls
PROPOSED IMPROVEMENTS
New Outfall #1
New Outfall #2
Larger Pipe
Expanded System
Larger Pipe

## Slide 15
proposed conditions 1-yr storm
The proposed improvements eliminates flooding throughout the neighborhood for the current 1-year storm event.
CB3566
CB1219

## Slide 16
proposed conditions 2-yr storm
The proposed conditions eliminates flooding throughout the neighborhood for the current 2-year storm event.
CB3566
CB1219

## Slide 17
proposed conditions 10-yr storm
The proposed conditions eliminates flooding on some streets and reduces flood depths and durations throughout the neighborhood for the current 10-year storm event.
CB3566
CB1219

## Slide 18
All roadways within the Riverside neighborhood are serviced by the proposed stormwater drainage system.
The proposed stormwater drainage system eliminates flooding throughout the neighborhood under the current 1 and 2-year storm events.
The proposed drainage system eliminates flooding on some streets and reduces flood depths and durations throughout the neighborhood under the current 10-year storm event.
Rainfall events and sea levels are predicted to increase in the future due to a changing climate, impacting the effectiveness of the proposed improvements.
Current climate Proposed Conditions results summary

## Slide 19
Under Future Conditions, tides get higher and rainfall intensity increases.
future conditions
The stormwater model was run with current climate and future climate conditions.
Rainfall (in) | Future Climate Conditions |  | 
24-hour Duration | Return Period (years) |  | 
 | 1-Year | 2-Year | 10-Year
Current Climate | 2.57 | 3.19 | 5.04
Year - 2050 | 3.1 | 3.9 | 6.2
Year - 2070 | 3.5 | 4.3 | 6.8
Tides | Future Climate Conditions |  | 
Elev. NAVD88 | Tidal Event |  | 
 | MLW | MHW | Dec-2022
Current Climate | -5.17 | 4.33 | 8.34
Year – 2050 | -2.3 | 7.3 | NA
Year – 2070 | -0.7 | 9.2 | NA
Mills Ave Roadway Cross Section
Roadway Elev. ~7.3 ft

## Slide 20
Existing conditions 2050 PROJECTED 1-yr storm
The projected 2050 tidal increases overtop the roadway of Mills Avenue and flood neighborhood.
2050 MHW =
EL. 7.3 NAVD88
Maximum inundation extents for 2- & 10-year storm events are similar to the depicted 1-year event.

## Slide 21
Existing conditions 2070 PROJECTED 1-yr storm
2070 MHW =
EL. 9.2 NAVD88
The projected 2070 tidal increases significantly overtop the neighborhood.
Maximum inundation extents for 2- & 10-year storm events are similar to the depicted 1-year event.

## Slide 22
This phase of design focused on analyzing drainage improvements without the addition of a coastal berm.
Due to the elevation and vulnerability of the community, the design’s effectiveness is impacted by projected future conditions with increased precipitation and tidal elevations.
  Without a coastal berm, the projected future tidal elevation is projected to be at or above the Mills Ave roadway elevations.
PROPOSED IMPROVEMENTS Challenges
Table or figure showing elevations compared to road
BERM
Roadway Elev. ~7.3 ft
Roadway Elev. ~7.3 ft
Roadway Elev. ~7.3 ft
Mills Ave Roadway Cross Section

## Slide 23
Proposed conditions 2050 PROJECTED 1-yr storm
2050 MHW =
EL. 7.3 NAVD88
The projected 2050 tidal increases overtop the roadway of Mills Avenue and flood neighborhood.
Maximum inundation extents for 2- & 10-year storm events are similar to the depicted 1-year event.

## Slide 24
Proposed conditions 2070 PROJECTED 1-yr storm
The projected 2070 tidal increases significantly overtop the neighborhood.
2050 MHW =
EL. 7.3 NAVD88
Maximum inundation extents for 2- & 10-year storm events are similar to the depicted 1-year event.

## Slide 25
The influence from future sea level rise significantly impacts the effectiveness of the proposed improvements.
Projected future increases to tidal elevations (2050 & 2070) will overtop Mills Ave and the neighborhood more frequently.
The proposed drainage system improvements will provide temporary improvements.
Without additional coastal protection such as a coastal berm, the proposed drainage system loses its benefit as the ocean begins to rise and overtops Mills Ave roadway overwhelming the maximum proposed improvements.
future climate results summary

## Slide 26
Continue to evaluate stormwater model results
Formulate recommendations based on results.
Prepare Cost Analysis.
NEXT STEPS
Riverside Neighborhood, Revere, Massachusetts

## Slide 27
Project Contacts:
Elle Baker – City of Revere - ebaker@revere.org
Scott Turner – Fuss & O’Neill – Scott.Turner@fando.com
Thank You